# L A M A R   C O U  N T Y

## Request For Bid

Backhoe

Bid No. RE-0321-1

## Return Deadline is NOT LATER THAN:  9:00 A.M., April 14, 2021

RETURN SEALED BID TO:

Lamar County Auditor

119 N. Main, Room B05

Paris, Texas  75460

### REQUEST FOR BID

NEW BACKHOE

FOR PRECINCT THREE

- GENERAL INSTRUCTIONS TO VENDORS

- The Commissioner’s Court of Lamar County will receive bids until 9 A.M.,

Wednesday, April 14, 2021 for the purchase of a new wheeled excavator.

- Lamar County appreciates your time and effort in preparing a bid.  Please note

all bids must be received at the designated location by the deadline shown.  Bids received after deadline will be returned unopened and shall be considered void and unacceptable.  Opening is scheduled to be held in the Commissioner’s Courtroom, 1st Floor, Courthouse, Paris, Texas.

- The Commissioner’s Court reserves the right to reject any or all bids and to waive

minor technicalities.

- Bids should be sealed and labeled “BID – WHEELED EXCAVATOR” and should be sent

to   the County Auditor’s Office, 119 N. Main, Room B05, Paris, Texas  75460.

- To obtain results, or if you have any questions, please contact the Lamar County

Auditor’s Office at (903)737-2416.

- Bids to be acceptable for consideration must conform to the following instructions

and specifications.

#### III.  SPECIFICATIONS

FOR BACKHOE

Specifications:	The Backhoe requested shall include

Weight –

- Minimum 40,000 lbs

Engine –

- 4 cylinder, 161 horsepower @1800 rpm, turbo charged

- Engine idle sensor controlled

- Bore/Stork 4.1/5,2 in 3

- Displacement 2746.3 in 3

- Engine Tier 4 Final

- Engine designed and produced by equipment manufacturer

Transmission –

- Oversized two speed power shift transmission with additional creeper    speed, axial piston motor with functional brake valve on both sides

- Maximum travel speed not less than 18.6 mph

- Manual or automatic hydraulically controlled front axle oscillation lock

- Automatic digging brake works automatically when acceleration pedal is engaged and when the machine is stationary

Hydraulics –

- Equipment and travel with axial piston variable displacement pump

- Hydraulic pump regulation and control with electronic engine speed sensing regulation, pressure and flow compensation, and torque-controlled swing drive priority

- Minimum 41 gallon hydraulic oil tank

- Minimum 92.5 gallon hydraulic system

- Minimum flow 79 gallons per minute

- Minimum max pressure 5,076 psi

- High pressure hydraulics circuit capable of powering a highspeed attachment

- High pressure circuit, permanent drive

Boom Stick and Performance –

- 2 piece boom 17’3” minimum length and 8’8” minimum stick length

- Maximum reach at ground level not less than 31’2”

- Maximum digging depth not less than 19’8”

- Maximum bucket breakout force with standard bucket not less than 22,346 lbf

- Maximum digging force not less than 16,141 lbf

- Pipe fracture safety valve on hoist cylinders and stick cylinders

Swing Mechanism –

- Maximum swing speed not less than 10 rpm

- Swing torque not less than 39,828 lbf ft

Outriggers –

- 4 Front and rear independently controlled outriggers

Operator’s Cab –

- Overall unit to match current wheeled excavator in Lamar County equipment inventory (inspection of current equipment can be arranged by calling Commissioner Bass at 903-249-6237)

- Road, tail and turn lights

- Falling objects guards

- Air suspension seat

- Sliding door window

- Air conditioner

- All hydraulic controls locked out when console is in raised position

- Travel alarm

- Rear view camera

- Side space monitoring camera

- Impact resistant cab glass

General –

- Automatic central lubrication of upper carriage

- Central lubrication of undercarriage, manual (centralized grease points)

Can Meet or Exceed These Specifications			 ______YES _____NO

###### STATE ORIGINAL PURCHASE PRICE: $_____________________________________________

STANDARD WARRANTY:

Describe standard warranty:__________________________________________________

_________________________________________________________________________

_________________________________________________________________________

DELIVERY TIME:__________days

BIDDER DOES (   )  DOES NOT (   ) MEET ALL SPECIFICATIONS

EXCEPTIONS:___________________________________________________________________

____________________________________________________________________

____________________________________________________________________

ADDITIONAL INFORMATION ON AVAILABLE LOADER: _________________________________ ______________________________________________________________________________________________________________________________________________________________

FIRM / BIDDER:__________________________________________________________________

BY:____________________________________________________________________________
	SIGNATURE								TITLE

ADDRESS:______________________________________________________________________

_______________________________________________________________________________

PHONE:_______________________________________   DATE:__________________________